## Slide 1: Searching for Litter with Computer Vision
Julian Hernandez
Mentor: Dr. Fitzgerald
California State University, Sacramento
MKN Heartland McNair Conference
September 2022

## Slide 2: The Trash Problem
Causes harm to wildlife
Contaminates soil and ground water
Costs a lot of money to recycle
Releases green-house gas emissions

## Slide 3: Early Trash Detection
An android app uses computer vision to classify trash into 6 material types on a blank background
A prototype trash cleanup robot designed to clean up trash in grassy areas showed promising results

## Slide 4: California Regulations
In 2015 new regulations Department of Water Resources require cities to measure plastics
San Francisco Estuary Institute (SFEI) uses computer vision to “find the best ways to filter their stormwater and stop contaminants such as trash and plastics from entering their protected wetlands and public waterways” Hale

## Slide 5: The Problem: Quickly Measuring Trash
How do we measure trash now?
Qualitative: Site scoring uses average assessments to score a site from 1-12
  “this method is subjective and depends on the assessor’s perception of trash conditions” (SFEI)
Quantitative: Volume based approach is more precision but requires a lot of time and resources
  Up to 3 hours 30 minutes for a 300ft site

## Slide 6: Unoccupied Aerial Vehicle (UAS) Count
UAS systems sped up counting process
Best accuracy came from lower flights
  The closer the object the easier to identify
More images would be needed for increased accuracy
Field Testing Report - Trash Monitoring Methods

## Slide 7: Goal of this Research
Can computer vision quantify street-side litter from collected images?
Detect trash
Plot detections
Geolocate items
Collect images
& datasets

## Slide 8: Street Level Images: Mapillary
Began collecting dashcam footage in 2013
Coverage for the 190 countries’ road networks
Sample Mapillary image with trash
Mapillary image cover near Sacramento State University

## Slide 9: Cleanup Images
Collected 150 images from around Sacramento State University
Can be taken on any smartphone or handheld device
Coordinates and other metadata are automatically stored

## Slide 10: Mask Regional Convolutional Neural Network (Mask R-CNN)
Facebook releases a plugin using Mask R-CNN to suggest building outlines for OpenStreetMap
  Building shapes were used as training data, allowing it predict new rooftop outlines
Training data (Red)
Training data (Red)
Mask R-CNN predictions (Purple)

## Slide 11: Trash Annotations in Context Dataset (TACO)
Researchers pre-trained multiple Mask R-CNN models on 1,500 annotated images
We selected 10 categories

## Slide 12: Localization
EXIF metadata contains photo coordinates, camera orientation, date and time, etc
Depth must be derived from object size
  Pedro F. Proença (co-author of TACO dataset) went on to research RGBD (Red, Green, Blue, and Depth)

## Slide 13: Metrics
Precision
Recall
 | Positive | Negative
True | True Positive (TP) | True Negative (TN)
False | False Positive (FP) | False Negative (FN)

## Slide 14: Previous Results
TrashNet precision with video:
  Precision: 68%
  Recall: 69%
National College of Ireland:
  Precision: 69%
  Recall: 69%
AuqaVision based on TACO:
  Precision: 81%
  Recall: Not reported
SFEI Field Testing Report:
  Precision: 4%
  Recall: 10%

## Slide 15: Results
River Cleanup: Precision = 81% Recall = 74%
Mapillary: Precision = 1% Recall = 3%
Why did the algorithm perform as expected with smartphone images while failing to do the same with Mapillary images?
Mapillary dash cams
Smartphone images

## Slide 16: Problems
Low resolution Mapillary images
  Less pixels = more noise
Model was overfit to TACO dataset
  The dataset needs more diverse images
50% of false positives were from car misclassifications alone
  Common features: Texture, color, and shape

## Slide 17: Dataset & Model Improvement
TACO is based on COCO but is ~200x smaller
Trash Annotations in Context (TACO):
  1,500 images
  4,700 outlined objects
Common Objects in Context (COCO):
  300,000 images
  2,000,000 outlined objects

## Slide 18: Model Feedback
Train model on a diverse set of images from smart phones, drones, dashcams, mounted cameras, etc.
Continually update database with new images so that the algorithms is constantly developing

## Slide 19: Application: Quantify Zero Waste Efforts
How do cities measure the effectiveness of waste management policies?
Measure the starting amount of trash in the environment to establish a baseline
Quantify clean up totals and compare this against the baseline counts
Allow researchers to look at geographic trends over time

## Slide 20: Future Work
How to deploy trash detection models to make real world improvements?

## Slide 21: Smart Composting & Recycling
Does suggesting the correct bin increase recycling rates?
California has a “42% recycling/composting rate in 2020, up from 37% the year before. California’s goal for 2020 had been 75%, however.” resource-recycling.com

## Slide 22: Measuring plastic in Waterways
How can the amount of trash entering and exiting the waterways be monitored?
Work with recollect, City of Sacramento, San Francisco Estuary Institute (SFEI)

## Slide 23
What is the problem?
  Measuring trash levels must either be done quickly or accurately
How do we fix this?
  By automating the process of labeling and plotting images, volunteers can assess a site much faster and with higher accuracy
How will this help?
  Enable cities to measure the effectiveness of zero waste policies

## Slide 24: Questions?
References available by email julianofhernandez@csus.edu